## Slide 2: Presentation Outline
Introduction
  Lidar Overview
  Study Areas
  Field Data Summary
  Lidar Data Summary
Applications
  Understory Vegetation Cover Prediction
  Individual Snag Detection
  Improving Plot-Level Standing Biomass Prediction
Current Work
  Towards Using Lidar Derived Information in a Forest Planning & Monitoring Setting

## Slide 3: Airborne Lidar Scanning
Active Remote Sensing Technology
  Directly Measures Heights
Two Types
  Full-Waveform
  Discrete-Return

## Slide 4: Airborne Lidar Scanning
Active Remote Sensing Technology
  Directly Measures Heights
Two Types
  Full Waveform
  Discrete-Return

## Slide 5: Airborne Discrete-Return Lidar
Small-Footprint
  Beam Diameter: 10-100 cm
Multiple Returns per Pulse
  Typically 2-3 returns max.
Accuracy
  Vertical < 30 cm
  Horizontal < 30 cm
Products
  Precise X, Y, Z Points
  Intensity

## Slide 6: Airborne Discrete-Return Lidar
Intensity
  Power of Returned Light
    Power Emitted
    Path Distance
    Intersected Object Surface Characteristics
  Commonly Not Utilized
    Calibration Variability
  Displayed Promise

## Slide 7: Study Locations

## Slide 8: Blacks Mountain Experimental Forest (BMEF)

## Slide 9: Storrie Fire (SF)

## Slide 10: Field Data Summary (2009)
Standing Trees (805 m2)
  DBH (cm)
  Height (m)
  Species
  Risk Rating
  Seedlings & Saplings Tallied (40.5 m2)
Understory Vegetation (40.5 m2)
  Crown Width (m)
  Aver. Height (m)
  Location
  Crown Width (m)
  Ht. Live & Dead Crown
  Condition Codes
  Location
  Max. Height (m)
  Species

## Slide 11: Lidar Data Summary
Acquisition Survey Design (July, 2009)
  AGL: 900 m
  Scan Angle: ± 14o
  Side Lap > 50%
  Intensity Range: 1-255
  Variable Gain Setting
  > 105,000 pulses sec-1
BMEF Specifications
  Average Point Density: 6.9 m-2 (sd: 5.6)
  Vertical Accuracy: < 10 cm
  First & Single Returns: 90.2%
SF Specifications
  Average Point Density: 6.7 m-2 (sd: 5.9)
  Vertical Accuracy: < 15 cm
  First & Single Returns: 89.9%
  Beam Diameter:
  ~24 cm (narrow)
  Up to 4 returns pulse-1

## Slide 12: Applications
Understory Vegetation Cover
  Traditionally Difficult to Estimate & Predict (R2 < 0.4)
  Filtered Lidar Metric Increases Explanatory Power (R2 > 0.7)
  Cover Prediction ± 22%
Individual Snag Detection
  Traditionally Difficult to Quantify
    Irregular & Sparse Distribution
  Filtering Algorithm Identifies Snag Pts.
  Overall Detection Rate of 70.6% (± 2.9)
    Snags w/ DBH ≥ 38 cm
Live Above-Ground Biomass
  Filtered Point Cloud Improves Prediction

## Slide 13: Applications
Understory Vegetation Cover
  Traditionally Difficult to Estimate & Predict (R2 < 0.4)
  Filtered Lidar Metric Increases Explanatory Power (R2 > 0.7)
  Cover Prediction ± 22%
Individual Snag Detection
  Traditionally Difficult to Quantify
    Irregular & Sparse Distribution
  Filtering Algorithm Identifies Snag Pts.
  Overall Detection Rate of 70.6% (± 2.9)
    Snags w/ DBH ≥ 38 cm
Live Above-Ground Biomass
  Filtered Point Cloud Improves Prediction

## Slide 14: Introduction
Importance
  Wildlife Habitat
  Fuel Loading & Behavior
  Nutrient Cycling
  Competition Dynamics & Overstory Structure
Been Difficult to Predict
  Standing Tree Variables
    Canopy Cover, Basal Area
  Topographic Variables
    Slope; Aspect
  R2 Range: 0.2-0.45
Common Sampling Methods
  Ocular Estimation
  Line-Intersect
  Fixed Plot
Lidar Methods
  Very Limited

## Slide 15: Method Overview
Derive Field Understory Vegetation Cover Estimates
Derive Lidar Predictor Variables
Model Selection & Fitting
Leave-One-Out Cross Validation

## Slide 16: Field Methods
BMEF Only (All Plots Combined)
40.5 m2 Circular Plots (n = 154)
Individual Shrubs
  Two Crown Widths
  Average Crown Height
  Maximum Crown Height
  Location (Azimuth & Distance)
Seedlings & Saplings
  Seedlings > 0.3 m Height
  Saplings into Two DBH Classes (2.54 & 5.08 cm)
Understory Vegetation Cover
  GIS Shrub Layer
  Saplings:
    2.54 cm = 0.5 m2
    5.08 cm = 1.0 m2
  Seedlings: 0.15 m2

## Slide 17: Field Methods
BMEF Only
40.5 m2 Circular Plots (n = 154)
Individual Shrubs
  Two Crown Widths
  Average Crown Height
  Maximum Crown Height
  Location (Azimuth & Distance)
Seedlings & Saplings
  Seedlings > 0.3 m Height
  Saplings into Two DBH Classes (2.54 & 5.08 cm)
Understory Vegetation Cover
  GIS Shrub Layer
  Saplings:
    2.54 cm = 0.5 m2
    5.08 cm = 1.0 m2
  Seedlings: 0.15 m2

## Slide 18: Lidar Methods
Normalize Point Heights
Extract Plot Point Cloud
Derive Lidar Predictor Variables
  3 Understory Metrics
  40 Overstory Metrics
  7 Topographic & Stand Attribute Metrics
Understory Lidar Cover Density
  Define Understory Layer
  Extract Understory Points
  Apply Intensity Filter
  Apply Formula:

## Slide 19: Lidar Methods
Understory Lidar Cover Density
  Define Understory Layer
  Extract Understory Points
  Apply Intensity Filter
  Apply Formula:

## Slide 20: Lidar Methods
Understory Lidar Cover Density
  Define Understory Layer
  Extract Understory Points
  Apply Intensity Filter
  Apply Formula:
0
255

## Slide 21: Lidar Methods
Understory Lidar Cover Density
  Define Understory Layer
  Extract Understory Points
  Apply Intensity Filter
  Apply Formula:
0
255

## Slide 22: Modeling
Cover Data
  Bounded Between 0 and 1
  Heterskedasticity
Weighted Regression
  Weights Provide Proper Amount of Influence for Each Data Point
  Weights Estimated using Iterative Procedure
Beta Regression
  Well Suited for Proportions
  Extended Generalized Linear Model Approach

## Slide 23: Modeling
Cover Data
  Bounded Between 0 and 1
  Heterskedasticity
Weighted Regression
  Weights Provide Proper Amount of Influence for Each Data Point
  Weights Estimated using Iterative Procedure
Beta Regression
  Well Suited for Proportions
  Extended Generalized Linear Model Approach

## Slide 24: Model Comparison
Leave-One-Out Cross Validation
  Absolute Bias
  Root Mean Square Error

## Slide 25: Results
Models
LOO Cross Validation
Overall Prediction
Accuracy: ± 22%

## Slide 26: Results
Models
LOO Cross Validation
Overall Prediction
Accuracy: ± 22%
Model Performance Remains Stable to Canopy Cover
  Two Most Likely Causes:
    ULCD, is relative to the number of points that reach the understory.
    The likelihood of encountering understory vegetation decreases with increasing canopy cover for this forest type

## Slide 27: Results
Models
LOO Cross Validation
Overall Prediction
Accuracy: ± 22%
Model Performance Remains Stable to Canopy Cover
  Two Most Likely Causes:
    ULCD, is relative to the number of points that reach the understory.
    The likelihood of encountering understory vegetation decreases with increasing canopy cover for this forest type

## Slide 28: Discussion
Model Comparison
  Both Performed Well
  WR Simpler to Implement
  Might Perform Better w/ Different Models
    Zero-Inflated Beta Regression
Performance Dependent Upon
  Forest Type and Structure
  Intensity Data Quality
    Calibration
    Proportion of First & Single Returns
  Lidar Point Densities
Possible Improvements
  Field Derived Cover Estimates
  New Filtering Methods

## Slide 29: Products
Understory Vegetation Cover Maps
  Traditional Lidar Two-Stage Procedure
  Method Extends into Biomass, Volume and Fuel Characterizations

## Slide 30: Applications
Understory Vegetation Cover
  Traditionally Difficult to Estimate & Predict (R2 < 0.4)
  Filtered Lidar Metric Increases Explanatory Power (R2 > 0.7)
  Cover Prediction ± 22%
Individual Snag Detection
  Traditionally Difficult to Quantify
    Irregular & Sparse Distribution
  Filtering Algorithm Identifies Snag Pts.
  Overall Detection Rate of 70.6% (± 2.9)
    Snags w/ DBH ≥ 38 cm
Live Above-Ground Biomass
  Filtered Point Cloud Improves Prediction

## Slide 31: Introduction
Importance
  Wildlife Habitat
  Nutrient Cycling
  Long-Term Carbon Storage
  Key Indicator for Biodiversity
Minimum Stocking Standards
  Common Snag Thresholds: DBH ≥ 25 or 38 cm
Difficult to Quantify
  Distribution Highly Variable
  Requires Intensive Sampling
  Expensive to Sample

## Slide 32: Method Overview
Collect Field Snag Stem Map Data
  805 m2 Circular Plots (n= 206)(843 Snags)
Extract Height Normalized Plot Lidar Point Clouds
Apply Snag Filtering Algorithm
Create Lidar-Based Snag Stem Map
Compare Snag Stem Maps (Field vs. Lidar)
  Detection & Error Rates

## Slide 33: Field Methods
Both BMEF & SF
  BMEF Total Area Sampled: 12.5 ha (805 m2 Plots = 154)
  Storrie Total Area Sampled: 4.2 ha (805 m2 Plots = 52)
Individual Tree Measurements (DBH ≥ 9 cm) (Height ≥ 3 m)
  Species
  DBH (cm)
  Height (m)
  Location
  Condition Codes
  Snags: Decay Stage

## Slide 34: Snag Filtering Algorithm
Identifies Snag Points & Removes Live Tree Points
Local-area 2D & 3D Filters Based on Location and Intensity Values
Final Result: Point Cloud Containing Only Snag Points in the Overstory

## Slide 35: Snag Filtering Algorithm
Intensity Value Characteristics
  Snags
    High Percentage (> 90%) Low Intensity Points
    (0 – 75 i)
      Solid Woody Material (Bark, Bare, Charred)
    Some Snags had Small Percentage ( < 10%) High Intensity Points (> 135 i)
      Solid Bare Seasoned Wood (Light Colored – Reflective)
    Some Snags had Very Small Percentage of (< 10%) of Mid-Range Intensity Points (75 – 135 i)
      Dead Needles or Leaves, Fine Branches, Witches Broom
  Live Trees
    Mix of Low- and Mid- Range Intensity Values (0 – 135 i)
    Small Number of Live Trees had High Intensity Points (> 135 i)
      Trees with Sparse Crowns or Leader Growth

## Slide 36: Snag Filtering Algorithm
Lower & Upper Intensity Thresholds
Two Stages with Multiple Filters
  Elimination Stage
    Three 3D Filters to Remove Live Tree Points
  Reinstitution Stage
    Coarse-Scale 2D & 3D Filter
    Fine-Scale 2D Filter

## Slide 37: Individual Snag Detection
Create Canopy Height Surface Model
  ‘CanopyModel’ Program in Fusion Software Package
Locate & Measure Individual Snags
  ‘CanopyMaxima’ Program in Fusion Software Package

## Slide 38: Individual Snag Detection
Detection Criteria
  Within 2.5 m for Snags with Height < 9 m
  Within 4 m for Snags with Height ≥ 9 m
Error Rates
  Commission Error = Detected Snag when No Snag
  Omission Error = Undetected Snag

## Slide 39
BMEF Detection Rates
  ≥ 25 cm DBH Minimum Stocking Threshold 58% (± 4.3%)
  ≥ 38 cm DBH Minimum Stocking Threshold 62% (± 5.8%)

## Slide 40
Storrie Fire Detection Rates
  ≥ 25 cm DBH Minimum Stocking Threshold 76% (± 3.5%)
  ≥ 38 cm DBH Minimum Stocking Threshold 79% (± 4.6%)

## Slide 41: Results
Omission Errors
Commission Errors

## Slide 42: Detection Rate Trends

## Slide 43: Products
Snag Spatial Distribution
  Never Been Available w/out Intensive Sampling
  Many Forest Management & Assessment Applications
    Spatial Arrangement Assessments
    Wildlife Interactions
    Changes Over Time
Snag Density Estimates
  Stocking Standard
  Assessments & Clarity

## Slide 44: Conclusions
Filtering Affected By:
  Lidar Intensity Data Quality & Point Density
  Forest Structure & Canopy Density
New Filtering Methods Abound
Interesting Bi-Product: “Live Tree” Points

## Slide 45: Applications
Understory Vegetation Cover
  Traditionally Difficult to Estimate & Predict (R2 < 0.4)
  Filtered Lidar Metric Increases Explanatory Power (R2 > 0.7)
  Cover Prediction ± 22%
Individual Snag Detection
  Traditionally Difficult to Quantify
    Irregular & Sparse Distribution
  Filtering Algorithm Identifies Snag Pts.
  Overall Detection Rate of 70.6% (± 2.9)
    Snags w/ DBH ≥ 38 cm
Live Above-Ground Biomass
  Filtered Point Cloud Improves Prediction

## Slide 46
Methods
Compare Two Lidar Derived Metric Sets in Prediction of Live AGB
  Traditional
  Live-Tree (Dead Tree Points Filtered & Removed)
Regression Models Compared using Selection & Cross-Validation Statistics

## Slide 47
Airborne LiDAR Plot-Level AGB Prediction
  Derive a Myriad of Lidar Canopy Point Height Distribution Metrics
  Fit, Select, & Apply the Models
Lidar Biomass Methods

## Slide 48
Airborne LiDAR Plot-Level AGB Prediction
  Dead Tree Lidar Points Introduce Variability into Live AGB Models
Lidar Biomass Methods

## Slide 49
Results
VolCov = Lidar Canopy Cover * Lidar Mean Height
VolCov = 615
ln(LiveAGB) = β0 + β1ln(VolCov) + ε
VolCov = 444

## Slide 50
Results
Model Fit Statistics
LOO Cross Validation Statistics

## Slide 51
Point-Filtered Lidar Metrics (‘Live-Tree’) Reduced Variability
First Try… New Point-Filtering Methods Possible
Ability to Filter Points is Dependent on:
  Intensity Data Quality
    First & Single Returns Only!
  Point Density
  Forest Structure & Canopy Density
Future Work: Edge Point Filters & Weighting Schemes
Discussion

## Slide 52: Products

## Slide 53: Applications Summary
Demonstrates the Ability of Airborne Discrete-Return Lidar to Identify & Predict Unique Forest Attributes
Filtering Point Clouds Using Intensity and Location Information Provides Enhanced Framework
Possible Improvements:
  Calibrated Intensity Information
  New Filtering Methods
  Hyper- or Multi-spectral Imagery
  Small-Footprint Full-Waveform Lidar

## Slide 54: Current Work
Lidar Derived Information Can Successfully Predict Numerous Forest Attributes of Importance
  More Applications Developing Rapidly
Time to Incorporate into Forest Planning & Monitoring

## Slide 55: Current Work
Lidar Derived Information Can Successfully Predict Numerous Forest Attributes of Importance
  More Applications Developing Rapidly
Time to Incorporate into Forest Planning & Monitoring

## Slide 56
0.1011 ha Raster Grid Cell

## Slide 57
Forest Inventory
  Biomass / Volume
  BA
  Mean & Max Tree Height
  Canopy Cover & Closure
  Crown Class
  LAI
  QMD
  TPA
  FVS Tree List
  …
0.1011 ha Raster Grid Cell

## Slide 58
Forest Inventory
  Biomass / Volume
  BA
  Mean & Max Tree Height
  Canopy Cover & Closure
  Crown Class
  LAI
  QMD
  TPA
  FVS Tree List
  …
Fire/Fuels
  Canopy Fuel Weight
  Canopy Bulk Density
  Canopy Base Ht.
  Canopy Cover
  Mean & Max Ht.
  Ladder Fuels
  Surface Fuels
  …
0.1011 ha Raster Grid Cell

## Slide 59
Forest Inventory
  Biomass / Volume
  BA
  Mean & Max Tree Height
  Canopy Cover & Closure
  Crown Class
  LAI
  QMD
  TPA
  FVS Tree List
  …
Fire/Fuels
  Canopy Fuel Weight
  Canopy Bulk Density
  Canopy Base Ht.
  Canopy Cover
  Mean & Max Ht.
  Ladder Fuels
  Surface Fuels
  …
Wildlife Habitat
  Canopy Cover
  Canopy Structure
  Large Tree Counts (Live & Dead)
  Understory Shrub Cover
  CWD Presence
  Suitability Rating
  …
0.1011 ha Raster Grid Cell

## Slide 60
Wildlife Habitat
  Canopy Cover
  Canopy Structure
  Large Tree Counts (Live & Dead)
  Understory Shrub Cover
  CWD Presence
  Suitability Rating
  …
Forest Inventory
  Biomass / Volume
  BA
  Mean & Max Tree Height
  Canopy Cover & Closure
  Crown Class
  LAI
  QMD
  TPA
  FVS Tree List
  …
Fire/Fuels
  Canopy Fuel Weight
  Canopy Bulk Density
  Canopy Base Ht.
  Canopy Cover
  Mean & Max Ht.
  Ladder Fuels
  Surface Fuels
  …
Other
  Topographic
  Ecological
  Operational
  …
0.1011 ha Raster Grid Cell

## Slide 61: Current Work
High-Resolution Lidar-Derived Raster Dataset
  Provides Foundation to Optimize Forest Planning While Meeting Multiple Goals
  Possible to Add New Applications to Older Lidar Datasets
  Multiple Flights Will Likely Provide New Opportunities for G&Y Modeling

## Slide 62
Email: brianwing@fs.fed.us